## Slide 1
Dual Thermometer
Team VoltCrew

## Slide 2
Overview
Introduction
01
Device Architecture
02
Circuit Diagram
03
Bread Implementation
04
Our Team
05
06
08
Methodology
What is a thermister

## Slide 3
Introduction
Our team is developing a dual thermometer system that measures both body temperature and fluid temperature using two separate probes. The measured temperatures are processed using a microcontroller and displayed on a digital screen. The system relies on analog electronics to ensure accurate and reliable readings from each probe.

## Slide 4
A thermistor is a type of resistor whose resistance changes with temperature.
It is commonly used in temperature sensing applications. There are two main types of thermistors: NTC (Negative Temperature Coefficient), where resistance decreases as temperature increases, and PTC (Positive Temperature Coefficient), where resistance increases with temperature.
In our dual thermometer, NTC 10D-11, PT 100 thermistors are used to measure the temperatures from both the body and fluid probes, providing precise and responsive temperature readings.
What is a thermister ?

## Slide 5
Liquid temeperature input circuit
Body temeprature input circuit
Instrumentation amplifier
Output Display
Power supply
Device Architecture

## Slide 6
Circuit Diagram

## Slide 7
Power Supply Unit
  AC to AC Transformer (230V 30V double tap )
  Si Diodes-4
  Capacitors ( 470,0.1,10 microF)
  Zener Diodes (24,10,5.6)
  npn Transistor-1
  Resistors (10,50, 10, 100, 180, 470,2k, 5k, 10k)

## Slide 8
Linearization and Filter Circuit
  Input- PT100 thermister
  Linearization- 3 10k resistors
  LPF-1k resister-2, 10 microF capacitors-2
Body Temperature
Fluid Temperature
  Input- NTC 10k thermister
  Linearization- 3 100 ohm resistors
  LPF-1k resister-2, 10 microF capacitors-2

## Slide 9
Instrumentation Amplifier
  NE 5532 OPAMPs-3
  Resisters ( 10k-6, 6.6k-1 )

## Slide 10
Component | Reason
Transformer ( 230V to 30V double tap ) | According to the power requirement of the OPAMPs and other circuit components and proper functionality of the whole circuit
TL702 CP OPAMPs | Wide Supply Voltage Range Low Offset Voltage-ensures precise signal amplification High Slew Rate and Stability
TIP41C | Capability to switch currents up to 500 mA Maximum voltage rating (Vceo = 60V) allows it to handle a wide range of supply voltages without breakdown.
Instrumentation amplifier | High Accuracy and Noise Rejection Simplified Design-easy gain adjustment High Input Impedance-Prevents loading effects
Reasoning for Component Selection

## Slide 11
Component | Reason
NTC 10K thermistor for fluid | Wide Measurement Range
PT100 thermistor for body | Provides accurate and stable readings within the typical human body temperature range
Reasoning for Component Selection

## Slide 12
Breadboard Implentation

## Slide 13
Enclosure

## Slide 14
Enclosure

## Slide 15
Altium Design
Power Supply Unit
Amplifier Circuit

## Slide 16
Altium Design
Power Supply Unit
Amplifier Circuit

## Slide 17
PCB
Power Supply Unit
Amplifier Circuit

## Slide 18
Our Team
Luchitha Perera
Sanugi Wickramasinghe
Benul Wijerathna
Hansani Kaumadi

## Slide 19
THANK YOU!
Team
Volt Crew